## Slide 1: OutRAN : Co-optimizing for Flow Completion Time in Radio Access Network
Jaehong Kim, Yunheon Lee, Hwijoon Lim, Youngmok Jung, Song Min Kim, Dongsu Han
Notes: Hi, I’m Jaehong Kim, a 3rd year Ph.D student at KAIST.
In this talk, I will introduce our work called OutRAN,
which is a new scheduler that applies the concept of Flow Completion Time (FCT) to the cellular network.

## Slide 2: Interactive applications demand low latency.
Request (Uplink)
Remote Host
Radio link
(LTE/5G)
Response (Downlink)
100ms latency  1% profit loss ($3.8B)

## Slide 3: QoS provisioning defined in the standard
Background
Conversational
Interactive
RT Streaming
Low
High
Latency-sensitivity
The 3GPP defines multiple QoS classes with different priorities based on latency-sensitivity.

## Slide 4: QoS provisioning in current Cellular Networks
Background
Conversational
Interactive
RT Streaming
Best-effort
Dedicated QoS
(Guaranteed Bit Rate)
Low
High
Latency-sensitivity

## Slide 5: QoS provisioning in current Cellular Networks
4G/5G Core
xNodeB
Remote Hosts
Internet
User
Radio
Best-effort (Non-GBR)
Dedicated QoS (GBR)
Interactive
& Background
Interactive traffic shares the same quality of service with the background traffic.

## Slide 6: Problem of the existing base station scheduling
When short flows of the Interactive applications
co-exist with large background flows,
xNodeB
User
Short
Downlink
Best-effort
Remote Host
Large

## Slide 7: Problem of the existing base station scheduling
Latency-sensitive short flows could experience severe queueing delay.
Tx Complete
Queueing Delay

## Slide 8: Key enablers of achieving low latency in 5G
gNodeB
UE
Remote Hosts
Internet
1. Edgification of Servers and Core Networks  Reduces latency in backhaul
2. New Radio (NR) Interface  Brings low-latency in-air
5G NR
Air latency
MEC
Trasnport Latency

## Slide 9: The problem becomes significant in 5G.
Queueing delay at the base station still remains a problem in effectively reducing the end-to-end latency.
Queueing delay
gNodeB
5G NR
UE
MEC
Remote Hosts
Internet
Air latency
Trasnport Latency

## Slide 10: Preview: Impact of OutRAN in 5G
51% by MEC
Cell Load = 60%
28%
74%
Queueing delay prevents short flows from fully utilizing 5G's low latency.
27% by NR

## Slide 11: Cause #1: Large buffers in base stations
Base stations use large buffers (>10 x BDP[1,2]) for
bursty traffic, channel fluctuation, retransmissions.
xNodeB
Large queueing delay!
[1] An In-depth Study of LTE [SIGCOMM ‘13]
[2] Tackling Bufferbloat in 3G/4G Networks [IMC’12]

## Slide 12: Cause #2: Service-agnostic Scheduler
Designed to balance between spectral-efficiency and user fairness. (e.g., Proportional Fair scheduler)
Frequency
Time
xNodeB
Scheduler
Resource Block Allocation
Channel
Quality Report
(for efficiency)
Average throughput
(for fairness)
Buffer Status Report

## Slide 13: Problem of the existing base station scheduling
Latency-sensitive short flows could experience severe queueing delay.
Tx Complete
Queueing Delay

## Slide 14: Flow scheduling can achieve better latency
by completing latency-sensitive short flows first
 minimize Flow Completion Time (FCT)
Complete Short Flows First!

## Slide 15: Opportunity: Information-agnostic scheduling
Multiple-level Feedback Queue (MLFQ) [3,4,5] can
emulate Shortest Job First (SJF) without information.
[3] PIAS [NSDI’15]
[4] Aalo [SIGCOMM’15]
[5] AuTO [SIGCOMM’18]
Image credit: PIAS [3]

## Slide 16: Opportunity: Information-agnostic scheduling
High
Low
10MB
10MB
20KB
Threshold (20KB)
Multiple-level Feedback Queue (MLFQ) [3,4,5] can
emulate Shortest Job First (SJF) without information.
Image credit: PIAS [3]
[3] PIAS [NSDI’15]
[4] Aalo [SIGCOMM’15]
[5] AuTO [SIGCOMM’18]

## Slide 17: Unique characteristics in Cellular Networks
Different geographical locations and mobility
Users experience different channel quality across time.
UE 3
UE 1
Far
Close

## Slide 18: Case of applying the naive information-agnostic flow scheduling
Results in different scheduling decision from the legacy cellular scheduler.
UE 3
UE 1
Poor
Best
Best Channel
Quality
Shortest
Flow
UE3
UE2
Short Flows
UE1

## Slide 19: Side-effect of the naive approach
To get benefit, we need to tailor flow scheduling
for radio access network.
Hurts the spectral efficiency and user fairness.

## Slide 20: Scope & Goal of OutRAN
Target: downlink best-effort user traffic
Scope: downlink scheduling at the last-mile base station
Goal: co-optimize the Flow Completion Time (FCT) and key cellular scheduler metrics (e.g., spectral efficiency)
Remote Server
Flow Scheduling
xNodeB
Buffer
Best-effort, QoS Unavailable

## Slide 21: Challenge: Mismatch in optimization goals
Cellular network schedulers have different optimization goal;
ex) maximizing the radio resource utilization (or fairness).
Active Users
User with the Best channel quality
User having
Shortest flow
Legacy
Ours

## Slide 22: Challenge: How can we satisfy both goals?
Key idea: find the user-flows that best balance for both optimization goals.
Short Flows
Active Users
Excellent Channel Quality
Best Channel
OutRAN
Shortest Flow

## Slide 23: Design #1: Intra-user Flow Scheduler
Short Flows
Active Users
Best Channel
Shortest Flow
Effectively improves the FCT without any loss of the
legacy scheduler metrics.

## Slide 24: Design #1: Intra-user Flow Scheduler
Emulate SJF on the flows sharing the same user
(i.e., intra-user flows) using MLFQ.
MLFQ Scheduling
UE3
UE2
Short Flows
UE1
UE3
UE2
Short Flows
UE1
Packet scheduling

## Slide 25: Design rationale
We can switch between Intra-user Flows and maintain
the exact same spectral efficiency and user fairness.
Selected
Selected
UE3
UE2
Short Flows
UE1
UE3
UE2
Short Flows
UE1
Packet scheduling
: Packet scheduling
: Radio Resource Block scheduling

## Slide 26: Design rationale
Even if we don’t pick the shortest flow,
choosing any user-flow always improves the FCT.
Best Channel
Quality
UE3
UE2
Short Flows
UE1
: Queueing delay by large flow
Best Channel
Quality
Improvement
UE3
UE2
Short Flows
UE1

## Slide 27: Design #1: Intra-user Flow Scheduler
Short Flows
Active Users
Best Channel
Shortest Flow
Effectively improves the FCT without any loss of the
legacy scheduler metrics.
Best Channel
Quality
Improvement
UE3
UE2
Short Flows
UE1

## Slide 28: Design #2: Inter-user Flow Scheduler
Effectively improves the FCT imposing minimal impact on the legacy scheduler metrics.
Short Flows
Active Users
Excellent Channel Quality
Best Channel
Shortest Flow

## Slide 29: Exploring more opportunity
Exploit the case where users are experiencing a
similar channel quality (or per Resource Block metric).
UE 1
UE 2
Excellent
Best
UE 1
UE 2
Poor
Best
Heterogenous Users
Homogeneous Users

## Slide 30: Design #2: Inter-user Flow Scheduler
Excellent Channel
Quality
UE 1
UE 2
Excellent
Best
Homogeneous Users
Opportunistically prioritizes the user carrying
short flow among the homogenous user set if there’s any.
UE3
UE2
Short Flows
UE1
Packet scheduling

## Slide 31: Design #2: Inter-user Flow Scheduler
UE 1
UE 2
Excellent
Best
Homogeneous Users
Selected
Excellent
Opportunistically prioritizes the user carrying
short flow among the homogenous user set if there’s any.
UE3
UE2
Short Flows
UE1
: Packet scheduling
: Radio Resource Block scheduling

## Slide 32: Design #2: Inter-user Flow Scheduler
UE 1
UE 2
Poor
Best
Heterogenous Users
Best Channel
Quality
If we cannot find the homogenous users,
select the best one just like the original scheduler.
UE3
UE2
Short Flows
UE1

## Slide 33: Design #2: Inter-user Flow Scheduler
Instead of strictly selecting the user having the “best” per Resource Block metric (e.g., Channel Quality), expand the room by |ε|.
Short Flows
Active Users
Excellent Channel Quality
Best Channel
Shortest Flow
|ε|

## Slide 34: Integrating OutRAN into xNodeB
OutRAN also considers unique design aspects in xNodeB.
L1
PHY
MAC
RLC
PDCP
IP
xNodeB Radio Protocol Stack
Segmentation & reassembly
Retransmission
L2
L3
Header compression
Sequence numbering
Cipherying
Scheduling
Retransmission

## Slide 35: Implementation and Overview
Implemented on top of the srsRAN, open-source LTE/5G software radio suite.
L1
PHY
MAC
RLC
PDCP
Intra-user Flow Scheduler
L2
Flow identification
Flow state management
Inter-user Flow Scheduler
USRP B210
Linux Machine

## Slide 36: Evaluation Platforms
We evaluate OuRAN using a combination of testbed experiments and NS-3 simulations:
1. Over-the-air testbed
3. Cell scale NS-3 simulations
2. Colosseum wireless emulator

## Slide 37: Evaluation Platforms
Large-scale of users,
Advanced 5G settings
1. Over-the-air testbed
3. Cell scale NS-3 simulations
2. Colosseum wireless emulator
Realistic RF scenarios [6]
Mobile application
[6] SCOPE [MobiSys’21]

## Slide 38: Evaluation Setup
Traffic distribution : downlink cellular traffic dist collected in realworld eNodeBs [1]
Channel dynamics: 3GPP pedestrian scenario
Baselines : Proportional Fair (PF), SRJF, QoS-aware (CQA, PSS)
Metrics: Page load time (PLT) and FCT
Downlink cellular traffic distribution [1]
Channel quality distribution
[1] An In-depth Study of LTE [SIGCOMM ‘13]

## Slide 39: PLT Improvement
OutRAN shows an average 14% (up to 34%) reduction in PLT for the top 20 webpages from Alexa.

## Slide 40: FCT Improvement: Short Flow FCT
OutRAN shows comparable short flow FCT to that of the SRJF and QoS-aware schedulers.
OutRAN works well without prior information.
Better
Short Flow (< 10KB) 95%-ile
QoS-aware
de-facto standard

## Slide 41: What about Long Flow FCT?
Unlike SRJF, OutRAN considers both spectral efficiency and flow size. It does not starve long flows.
Long Flow (> 0.1MB) FCT
Worst due to channel-unaware scheduling
Better

## Slide 42: Spectral-efficiency and user fairness
OutRAN preserves 98% and 97% of spectral efficiency and fairness respectively that PF provides.

## Slide 43: Scalability
OutRAN has the same computational complexity as the original scheduler. It can scale and handle large number of flows.

## Slide 44: Impact of OutRAN in 5G
Scheduling resolution
15kHz
60kHz
120kHz
30kHz
1ms
500us
250us
125us
Low-latency in air
OutRAN is compatible with 5G NR, provides greater improvement in short flow FCT when utilized together.
Numerology 0
Numerology 1
Numerology 2
Numerology 3
Better

## Slide 45: Conclusion
OutRAN demonstrates the feasibility of co-optimizing the FCT in cellular networks.
It achieves better latency for interactive application by scheduling its short flows first at the last-mile base station.
It is practical; it does not require prior QoS information and respects the legacy cellular metrics.
https://ina.kaist.ac.kr/projects/outran/

## Slide 46: Thank you Questions ?